My Baby’s Got LED Controller Board
mcqn.com/ibal223/

Getting Started
1. Connect your lights to the My Baby’s Got LED controller: either with the 3-pin header, or the green terminal block. Make sure to check the polarity! If you’re running a lot of lights, then use the green terminal block’s 5V and Gnd connections to run extra power lines, in addition to the 3-pin header.
2. Plug your PC power supply into the white Molex connector on the underside of the My Baby’s Got LED controller board.
3. Plug in and power on your PC power supply. The “LED Power” light should illuminate on the controller board; the first 30 LEDs on your LED strip will light up amber; and the “WiFi” light on the controller board will fade on and off.
4. The pulsing “WiFi” light means that the board isn’t connected to WiFi. It will create a new WiFi network called “WLED-AP” with a password of “wled1234”. Connect to that with your phone or computer.
5. You’ll be redirected to the WLED welcome page, from there you can control the lights directly
Connecting the Controller to Your Network
1. Run through the steps in “Getting Started” above.
2. When you get to the WLED welcome page, choose the “WiFi Settings” option.
3. Enter the details of your WiFi so that it can connect to your network (then you’ll be able to control it from any computer/phone on your network) but DO NOT click on save just yet!
4. Find the mDNS setting. You might want to give your controller board a better mDNS name so it’s easier to connect to from your network. At the very least you should make a note of the name, as you’ll need it in a moment.
5. Now you can save the settings by clicking “Save & Connect”.
6. Connect back to your network with your phone/laptop (usually this happens automatically when the controller board turns off the WLED-AP network.
7. In a web browser, go to the name that you made a note of in step 4.
8. Now you can control the lights as before.
Status Lights

The My Baby’s Got LED controller board has three status lights:

- WiFi – This shows the status of the WiFi connection. If it is solid then the board is connected to WiFi. If it’s pulsing on and off, then the board can’t find the WiFi and has created its own WiFi.
- LED Power – This shows when power is turned on to the LEDs (and when the ATX power supply is turned on, rather than just in standby).
- Network – This shows when the controller has a connection to an MQTT broker, as configured in the “Sync Interfaces” page in the settings.

Factory Reset

Pressing the “Reset” button on the controller will restart the software. If you hold the reset button down for more than 5 seconds it will perform a factory reset, which clears any settings that you’ve added.

More Information

There’s lots more information about the WLED software available at https://github.com/Aircoookie/WLED/wiki
If you have any other questions, drop us a line at info@mcqn.com.